## Slide 1: Operating Systems

## Slide 2
18. Paging: Introduction

## Slide 3: Concept of Paging
Paging splits up address space into fixed-zed unit called a page.
  Segmentation: variable size of logical segments(code, stack, heap, etc.)
With paging, physical memory is also split into some number of pages called a page frame.
Page table per process is needed to translate the virtual address to physical address.

## Slide 4: Advantages Of Paging
  Flexibility: Supporting the abstraction of address space effectively
  Don’t need assumption how heap and stack grow and are used.
Simplicity: ease of free-space management
  The page in address space and the page frame are the same size.
  Easy to allocate and keep a free list

## Slide 5: Example: A Simple Paging
128-byte physical memory with 16 bytes page frames
64-byte address space with 16 bytes pages
0
16
32
48
64
(page 0 of the address space)
(page 1)
(page 2)
(page 3)
A Simple 64-byte Address Space
0
16
reserved for OS
page 3 of AS
(unused)
page 0 of AS
(unused)
page 2 of AS
64-Byte Address Space Placed In Physical Memory
(unused)
page 1 of AS
32
48
64
80
96
112
128
page frame 0 of physical memory
page frame 1
page frame 2
page frame 3
page frame 4
page frame 5
page frame 6
page frame 7

## Slide 6: Address Translation
Two components in the virtual address
  VPN: virtual page number
  Offset: offset within the page
Example: virtual address 21 in 64-byte address space
Va5
Va4
Va3
Va2
Va1
Va0
VPN
offset
0
1
0
1
0
1
VPN
offset

## Slide 7: Example: Address Translation
The virtual address 21 in 64-byte address space
0
1
0
1
0
1
VPN
offset
1
1
0
1
0
1
PFN
offset
1
Virtual
Address
Physical
Address
Address Translation

## Slide 8: Where Are Page Tables Stored?
Page tables can get awfully large.
  32-bit address space with 4-KB pages, 20 bits for VPN
    Page offset for 4 Kbyte page: 20 bit
Page tables for each process are stored in memory.

## Slide 9: Example: Page Table in Kernel Physical Memory
0
16
page table
3 7 5 2
page 3 of AS
(unused)
page 0 of AS
(unused)
page 2 of AS
Physical Memory
(unused)
page 1 of AS
32
48
64
80
96
112
128
page frame 0 of physical memory
page frame 1
page frame 2
page frame 3
page frame 4
page frame 5
page frame 6
page frame 7

## Slide 10: What Is In The Page Table?
The page table is a data structure that is used to map the virtual address to physical address.
  Simplest form: a linear page table, an array
The OS indexes the array by VPN, and looks up the page-table entry.

## Slide 11: Common Flags Of Page Table Entry
Valid Bit: Indicating whether the particular translation is valid.
Protection Bit: Indicating whether the page could be read from, written to, or executed from
Present Bit: Indicating whether this page is in physical memory or on disk(swapped out)
Dirty Bit: Indicating whether the page has been modified since it was brought into memory
Reference Bit(Accessed Bit): Indicating that a page has been accessed

## Slide 12: Example: x86 Page Table Entry
P: present
R/W: read/write bit
U/S: supervisor
A: accessed bit
D: dirty bit
PFN: the page frame number
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
PFN
G
PAT
D
A
PCD
PWT
U/S
R/W
P
An x86 Page Table Entry(PTE)

## Slide 13: Paging: Too Slow
To find a location of the desired PTE, the starting location of the page table is needed.
For every memory reference, paging requires the OS to perform one extra memory reference.

## Slide 14: Accessing Memory With Paging
1 // Extract the VPN from the virtual address
2 VPN = (VirtualAddress & VPN_MASK) >> SHIFT
3
4 // Form the address of the page-table entry (PTE)
5 PTEAddr = PTBR + (VPN * sizeof(PTE))
6
7 // Fetch the PTE
8 PTE = AccessMemory(PTEAddr)
9

## Slide 15: Accessing Memory With Paging
10 // Check if process can access the page
11 if (PTE.Valid == False)
12 RaiseException(SEGMENTATION_FAULT)
13 else if (CanAccess(PTE.ProtectBits) == False)
14 RaiseException(PROTECTION_FAULT)
15 else
16 // Access is OK: form physical address and fetch it
17 offset = VirtualAddress & OFFSET_MASK
18 PhysAddr = (PTE.PFN << PFN_SHIFT) | offset
19 Register = AccessMemory(PhysAddr)

## Slide 16: A Memory Trace
int array[1000];
...
for (i = 0; i < 1000; i++)
array[i] = 0;
prompt> gcc –o array array.c –Wall –o
prompt>./array
0x1024 movl $0x0,(%edi,%eax,4) //[edi+eax*4]= 0
0x1028 incl %eax
0x102c cmpl $0x03e8,%eax //0000 0011 1110 10002 = 100010
0x1030 jne 0x1024
Memory access

## Slide 17: A Virtual(And Physical) Memory Trace
Page Table[39]
Page Table[1]
1024
1074
1124
1174
1224
Page Table(PA)
Code(PA)
4096
4146
4196
1024
1074
1124
Code(VA)
0
10
20
30
40
50
Array(PA)
7232
7282
7132
Array(VA)
40000
40050
40100
mov
mov
inc
cmp
jne
Memory Access
(PTE for data: 40000 / 1024)
(PTE for code: 1024 / 1024)